## Slide 1: E-bike
ME: Braden, Nyaire
EE: Cutter, Daniel
Programming: Daniel

## Slide 2: SPECS
Top speed: 30mph
Max weight: 350lbs
Max range: 45 minuets
0-30 time: 10 seconds

## Slide 3: Known Components
Frame
Tires
Seat
Transmission system
Motor
Braking system
Speedometer
MCU
Throttle
Battery
Footrests
Fuel Gage

## Slide 4: Components we have
Frame
We will be using an old mountain bike frame we have; it should be able to sustain street riding with the loads we expect as it was designed for aggressive terrain and benefits from a solid frame and dual shock absorption suspension.
Tires
There is another bike with hybrid/commuter tires that we will be fitting onto the chosen bike frame.
Transmission
Currently, we will be using the gears already on the bike frame and will adjust the gear ratio manually. This is just a launching point to meet our minimum requirements and can be developed into a more sophisticated system later.

## Slide 5: Brake System
Break Type: dual piston mechanical disk break
Location: front and back tires
Average Cost: $50
Range: $40-$200
Operation:
  When you squeeze the brake lever, you pull on the steel cable.
  The cable pulls a lever arm on the brake caliper.
  The lever arm pushes both brake pads toward the spinning brake rotor.
  The pads create friction against the rotor, slowing the wheel down.
Cumulative Total Estimated Cost: $50

## Slide 6: Motor Design
We will be using a high RPM DC motor. Using different gear ratios, we can get the high RPM motor to deliver significant torque to the wheel.
Required torque: 50-80 Nm
Estimated cost of motor: between $100-200
Controlled by a throttle input interpreted through an MCU
Air cooling should be sufficient; we will have to implement temperature safety mechanisms ourselves
Choice: 1/4 HP 24 Volt DC 1500 RPM Motor ($130)
Cumulative Total Estimated Cost: $180

## Slide 7: Battery
Minimum Wh: 780
Cost: $200-$500
NOTE: It may be slightly cheaper to build a battery with cells, but the difference (if there is any) is not worth it for the risk and effort required, therefor, we will be buying a battery.
Choice: 48V x 17.5 Ah Lithium Ion Battery ($200)
  Weight: 9.26 lbs
  Energy: 840 Wh
  Due to the open-air design of the frame air cooling should be sufficient during operation, although the battery might get hot during charging or very long uptimes
Cumulative Total Estimated Cost: $380

## Slide 8: Throttle System
Throttle Type: Ride-by-wire system
Type: half-twist throttle grip
Location: Right handlebar
Average cost: $40
Range: $8-$100
Operation:
  Rider Input: The rider twists or pushes the throttle.
  Signal Generation: The Hall-effect sensor inside the throttle generates a corresponding voltage signal.
  Signal Interpretation: The controller receives the signal and interprets it based on its programming. The controller acts like the system's "brain" and manages all power delivery.
  Power Delivery: The controller draws power from the battery and sends the appropriate amount of current to the motor.
  Acceleration: The motor responds by accelerating the bike. The process happens almost instantaneously, resulting in smooth, on-demand power.
Cumulative Total Estimated Cost: $420

## Slide 9: Speedometer
System will use two 8 segment digital number displays controlled by the onboard MCU. It will require some sort of sensor system to determine the linear speed of the bike, depending on the sensors required to operate the other systems we might not have to buy additional sensors to implement this feature.
Cumulative Total Estimated Cost: $450

## Slide 10: Proposed Budgets
Depending on the budget this project receives we can implement different features, here is what and how said features will be incorporated depending on the budget.
$500
Everything discussed so far can be developed with this budget. These are the things required to meet our minimum deliverables in a reasonable way and are non-negotiable.
$700-$1000
With this budget we can buy or develop an automatic shifting system that can fit onto the bikes existing derailleur system.
The higher end of this budget would be needed if we decided to buy a high end, pre-made shifting system, which is typically around $400.
$1400 - $1700
For this budget we would design an automatic shifting system to conserve money and have a more synchronized device.
The specs we would aim for with this budget would be a top speed of 60mph and a max weight of 400lbs. This would require better tires, a bigger motor or an advanced gearbox, a bigger battery, more safety features and sensors, and potentially a thicker sturdier frame.